|  | PRESS RELEASE |
| --- | --- |

Three fuel samples tested in March failed

(Prague, 15 May 2024) The Czech Trade Inspection Authority monitored the quality of fuels in March 2024. 249 samples were taken and three failed to meet the quality requirements. In the overall assessment, this represents 1.2% of non-compliant samples.

The Czech Trade Inspection Authority continued its regular checks on the quality of fuels. In March, it took a total of 249 fuel samples at petrol stations in the Czech Republic. Of these, 3 samples taken and checked did not meet the specified quality requirements, which represents 1.2% of non-compliant samples in the overall assessment.  These were three samples of motor gasoline.

| Collected fuel samples by types - April 2024 |
| --- |
| Fuel type | Collected samples | In % | Noncompliant samples | % of fuel type |
| petrol | 103 | 41,36 | 3 | 2,9 |
| diesel fuel | 112 | 44,98 | 0 | 0,0 |
| FAME | 0 | 0,00 | 0 | 0,0 |
| diesel fuel blebd | 0 | 0,00 | 0 | 0,0 |
| diesel fuel B10 | 0 | 0,00 | 0 | 0,0 |
| high FAME diesel fuel | 0 | 0,00 | 0 | 0,0 |
| paraffinic diesel fuel | 0 | 0,00 | 0 | 0,0 |
| LPG | 30 | 12,05 | 0 | 0,0 |
| CNG, bio-CNG | 4 | 1,61 | 0 | 0,0 |
| LNG, bio-LNG | 0 | 0,00 | 0 | 0,0 |
| Ethanol E85 | 0 | 0,00 | 0 | 0,0 |
| Total | 249 | 100,00 | 3 | 1,2 |

Motor gasolines

In March 2024, the Czech Trade Inspection Authority collected and inspected a total of 103 samples of motor gasoline. Of these samples taken, 3 samples did not meet the quality requirements of the relevant technical standard. One sample failed in the quality parameter 'ethanol', where the measured value of this quality parameter was 6,90 % v/v (the maximum value including measurement uncertainty is 5,21 % v/v). The second sample failed in the quality parameter 'octane number by research method', where the measured value of this parameter was 87,5 (the minimum value including measurement uncertainty is 94,6), in the quality parameter 'octane number by engine method', where the measured value of this parameter was 81,3 (the minimum value including measurement uncertainty is 84, 5), in the quality parameter 'evaporated quantity at 100 °C', where the measured value of this parameter was 44,0 % v/v (the minimum value when including the measurement uncertainty is 44,5 % v/v) and in the quality parameter 'end of distillation', where the measured value of this parameter was 317 °C (the maximum value when including the measurement uncertainty is 214 °C).

The third sample failed for the quality parameter 'ethanol', where the measured value for this quality parameter was 7,46 % v/v (maximum value including measurement uncertainty is 5,21 % v/v), and for the quality parameter 'total oxygen content', where the measured value for this quality parameter was 3,10 % m/m (maximum value including measurement uncertainty is 2,81 % m/m). The other samples of motor gasolines checked and analysed met the quality parameters set out in the technical standard ČSN EN 228+A1/Z2:2024 - Motor fuels - Unleaded motor gasolines - Technical requirements and test methods in relation to the requirements of Decree No 516/2020 Coll., on requirements for fuels and implementation of certain other provisions of the Law on fuels.

Biofuels in fuels

During the period under review, the fatty acid methyl ester content of 112 samples was checked

diesel fuel. The ethanol content of motor gasoline was checked in 102 samples out of 103 samples taken (1 sample was a repeat sample at the same service station and was not checked for ethanol content). Laboratory analyses revealed that the permissible upper limit for ethanol content was exceeded in 2 samples of motor gasoline.

Conclusion

In March 2024, 3 samples of motor gasoline failed, 1 more than in February. Compared to February, there was an improvement from 1.2% to 0.0% for diesel fuel samples collected and checked and from 10.5% to 0.0% for LPG samples collected and checked. FAME, blended diesel, B10 diesel, high FAME diesel, paraffinic diesel, bio-CNG, LNG, bio-LNG and E85 ethanol were not sampled in March 2024 due to fuel market developments. In the overall assessment and quality comparison of fuel samples taken in March 2024 compared to February 2024, an improvement from 2.9% to 1.2% in the number of non-compliant samples was observed.

Fuel quality control results by inspectorate:

| Inspectorate | Petrol | Diesel | LPG | CNG | Total |
| --- | --- | --- | --- | --- | --- |
|  | OD | N | OD | N | OD | N | OD | N | OD | N |
| Středočeský and Prague | 13 | 0 | 16 | 0 | 6 | 0 | 1 | 0 | 36 | 0 |
| Jihočeský and Vysočina | 16 | 1 | 16 | 0 | 6 | 0 | 0 | 0 | 38 | 1 |
| Plzeňský and Karlovarský | 16 | 0 | 16 | 0 | 6 | 0 | 1 | 0 | 39 | 0 |
| Ústecký and Liberecký | 15 | 0 | 16 | 0 | 0 | 0 | 0 | 0 | 31 | 0 |
| Královéhradecký and Pardubický | 16 | 0 | 16 | 0 | 0 | 0 | 0 | 0 | 32 | 0 |
| Jihomoravský and Zlínský | 13 | 1 | 16 | 0 | 6 | 0 | 1 | 0 | 36 | 1 |
| Olomoucký and Moravskoslezský | 14 | 1 | 16 | 0 | 6 | 0 | 1 | 0 | 37 | 1 |
| Total | 103 | 3 | 112 | 0 | 30 | 0 | 4 | 0 | 249 | 3 |

Legend: COLL = collectted, N = noncompliance