|  | PRESS RELEASE |
| --- | --- |

Three fuel samples tested in April failed

(Prague, 21 May 2024) The Czech Trade Inspection Authority monitored the quality of fuels in April 2024. 250 samples were taken, three samples failed to meet the specified quality requirements, which represents 1.2% of the total number of failed samples.

The CTIA continued its regular checks on the quality of fuels. It took a total of 250 fuel samples at petrol stations in the Czech Republic in April, of which 3 samples taken and checked did not meet the specified quality requirements, representing 1.2% of non-compliant samples in the overall assessment.  These were one sample of petrol, one sample of diesel and one sample of LPG.

Motor gasolines

In April 2024, 97 samples of motor gasoline were collected and inspected by the CTIA. Of this number, one sample did not meet the quality requirements of the relevant technical standard. The inspected sample failed in the quality parameter 'ethanol', where the measured value of this quality parameter was 8,72 % v/v (the maximum value including measurement uncertainty is 5,21 % v/v), and in the quality parameter 'total oxygen content', where the measured value of this quality parameter was 3,34 % m/m (the maximum value including measurement uncertainty is 2,81 % m/m). The other samples of motor gasolines checked and analysed met the quality parameters set out in the technical standard ČSN EN 228+A1/Z2:2024 - Motor fuels - Unleaded motor gasolines - Technical requirements and test methods in relation to the requirements of Decree No 516/2020 Coll., on requirements for fuels and implementation of certain other provisions of the Law on fuels.

Diesel fuel

In April 2024, the CTIA collected and inspected 112 diesel fuel samples. Of this number, one sample did not meet the quality requirements of the relevant technical standard. The inspected sample failed the quality parameter 'flash point', where the measured value was 29.5 °C (the minimum value when including the measurement uncertainty is 53.0 °C). The other samples of diesel fuel checked and analysed met the quality parameters set out in the technical standard ČSN EN 590/O1:2023 - Motor fuels - Diesel fuels - Technical requirements and test methods in relation to the requirements of Decree No 516/2020 Coll., on requirements for fuels and implementation of certain other provisions of the Fuel Act.

LPG

In April 2024, the CTIA collected and inspected a total of 37 LPG samples. Of this number of samples taken and inspected, one sample did not meet the quality requirements of the relevant technical standard. The inspected LPG sample did not comply with the quality parameter "sulphur", where the measured value of this quality parameter was 33.7 mg/kg (the maximum value when including measurement uncertainty is 31.1 mg/kg). The remaining samples of LPG checked and analysed met the quality parameters set out in the technical standard ČSN EN 589+A1:2022 - Motor fuels - Liquefied petroleum gases (LPG) - Technical requirements and test methods in relation to the requirements of Decree No 516/2020 Coll., on requirements for fuels and implementation of certain other provisions of the Fuel Act.

Biofuels in fuels

During the period under review, the fatty acid methyl ester content of 112 samples was checked

diesel fuel. The ethanol content of motor gasoline was checked in 97 samples. Laboratory analyses revealed that the permissible upper limit for ethanol content was exceeded in one sample of motor gasoline.

Measures

Pursuant to Section 7(1)(a) of Act No 64/1986 Coll., on the Czech Trade Inspection, the CTIA imposed in one case a measure consisting in a ban on the sale of diesel fuel which did not meet the quality and composition requirements laid down by the implementing legislation, special legislation and Czech technical standards. The measure was issued for 4 682.00 litres of petrol with a value of CZK 191 493.80.

Conclusion

Compared to March this year, CTIA inspectors noted an improvement in April in the sampled

and inspected samples of motor gasoline in April from 2.9% to 1.0%. A deterioration was recorded in the samples of diesel fuel collected and inspected from 0.0% to 0.9% and in the samples of LPG from 0.0% to 2.7%. FAME, blended diesel, B10 diesel, high FAME diesel, paraffinic diesel, bio-CNG, LNG, bio-LNG and E85 ethanol were not sampled in April 2024 due to fuel market developments. In the overall assessment and quality comparison of fuel samples taken, 1.2% of non-compliant samples were recorded in April as in March.

Fuel quality control results by inspectorate:

Legend: COLL = collected, N = noncompliant