|  | PRESS RELEASE |
| --- | --- |

"140 LED“ Christmas light chain poses a serious risk of electric shock

(Prague, 22 May 2024) The Czech Trade Inspection Authority has found that electrical equipment on the Czech market may pose a serious risk to consumers. The product in question is the "140 LED Christmas light chain".

The product was found to present a serious risk of electric shock or death to the user by the user touching accessible live parts of the product due to the removal of the power supply lead from the electronic unit or the removal of the cover of the electronic unit.

„140 LED vánoční světelný řetěz“

Product namee:  	                                           140 LED vánoční světelný řetěz

Model type / number:				LED Světelný řetěz/LAG-140LED

EAN:						not dispalyed

Identification data of manufacturer:                      not dispalyed

Identifikační údaje dovozce:		              not dispalyed

Distributor:	               HNC s.r.o., Sedlecká 748/7, 36010 Karlovy Vary

Země původu:	 China

It is a Christmas light chain with 140 non-replaceable LED light sources, equipped with an electronic unit in cardboard packaging. On the power cord, there is a label stating: light chain of 140 LEDs, 220-250V, 50Hz, max. power 6,5W, bulb type 3V, 0,03W, 0,01A, bulbs are not replaceable, number of bulbs 140pcs, made in China, distributor Lamer Fashion s.r.o. LAG-140LED, CE, IP20 and pictogram for indoor use only, mark for appliance protection of class II. On the packaging it says: 140 LED CHRISTMAS LIGHTS, made in China, distributor Lamer Fashion s.r.o., ADD: Libušská 319/126, Praha 4, 14200, CZECH REPUBLIC.

The product poses a serious risk because the power supply lead is not securely anchored to the electronic unit and sufficiently secured against pulling out. It is connected only by fusible material and soldering. Tampering with the lead may pull the lead out of the unit, exposing live parts of the product. The user may touch a live part of the product that is energized, and serious injury or death by electrocution may result. Another serious risk is the mechanical strength of the electronic unit, which is not sufficient. The cover can be easily removed from the controller by hand without force or tools, thereby exposing live parts of the product. If the user touches a live part of the product that is energized, serious injury or death to the user by electric shock will result.

The administrative authority, the CTIA Inspectorate of the Pilsen and Karlovy Vary Regions, imposed a protective measure on the seller pursuant to Section 50(3) of Act No. 90/2016 Coll., on Conformity Assessment of Selected Products when Made Available in the Market, as amended, which is a ban on the placing on the market of the above mentioned product, which is dangerous and which has already been placed on the market. The product is reported to the contact point at the MIT and information about it is published in the SAFETY GATE system.

Photos of the product: